## Slide 1: LISE++ pictures studio presents
FRIB/NSCL Staff Information Talk
How to Make Rare Isotope Beams at Home
04/04/2018
Oleg B. Tarasov

## Slide 2
Sense of humor
with all my deep respect for my scientific supervisor,
who has a great sense of humor,
who knows the story and some details of this presentation,
who helped me with the preparation,
but has not seen yet it.
I hope he’ll have fun.

## Slide 3: Keyword: “Home”
.. in Michigan…
Domestic research
How to Make Rare Isotope Beams at Home

## Slide 4
.. in Michigan…
Our case with rare beams at home will not create a danger to you, your housemates, your pets, your property, even your neighbors !!!
ISO 14001 Environmental management
Keyword: “Home”
How to Make Rare Isotope Beams at Home

## Slide 5: How I see that
after a hard day's work…

## Slide 6: Today is our day?

## Slide 7: May be the next time….
athlonsports.com

## Slide 8: Well-known Spartans fan
not in a good mood, we begin to quickly switch between channels
…. and suddenly!

## Slide 9: Nucleosynthesis and stellar evolution in the cosmos
Nuclear reactions in stars and stellar explosions generate energy and are responsible for the ongoing synthesis of the elements. They are, therefore, at the heart of many astrophysical phenomena, such as stars, novae, supernovae, and X-ray bursts.
MSUCL-1345
Sorry, I could not find the "original" voice, but at least this voice sounds without my Kirghiz accent

## Slide 10: Terra incognita
Terra Incognita
Around 260 stable isotopes found in nature (>1Gy)
Less than 1000 known isotopes in 1966, currently about 3000 (blue) know isotopes
New territory (Terra incognita) to be explored with next-generation rare isotope facilities as FRIB
They will produce more than 1000 NEW isotopes at useful rates (4500 available for study)
British accent.. Surprise!
Note, from slide to slide the cat is moving to the TV…

## Slide 11: 58Ca @ NSCL
What is last particle neutron-rich calcium isotope?
How do we produce rare isotopes?
What isotopes can be first observed in FRIB?
Let’s consider 58Ca isotope production as an example.
Why is 58Ca isotope? Magic Z=20, subshell at N=34
58Ca is the last* particle-bound neutron-rich calcium isotope, and furthermore was observed at the first time several years ago at MSU. (* officially)
May be it will useful to change the voice to a more pleasant one on the next page?

## Slide 12: You've Got Mail
Learn how to make rare isotope beams.
Do you know how to use email?
Then you can learn how to make a rare isotope.
It is that simple.
Learn how.
By the way, Brad came up with these phrases.

## Slide 13: L I S E ++
To estimate 58Ca isotope production we will use our powerful tool to prepare an experiment with rare isotope beams: the program LISE++
The LISE++ code has been developed to calculate the transmission and yields of fragments produced and collected in a spectrometer.
This is the last animated slide. Sorry for the following inconvenience ....

## Slide 14: LISE++ : Introduction
LISE++ is maintained by LISE++ group @ Michigan State University and is freely available and distributable through the LISE++ website: <http://lise.nscl.msu.edu>.
The LISE++ package (including codes PACE4, Global, Charge, MOTER, ETACHA4, Spectroscopic Calculator) operating on MS Windows environment
Currently the LISE++ software suite is undergoing a major transportation to a new graphics framework in order to support modern compilers and computing methods.
No hidden bitcoin mining procedures. Travis checked it recently.

## Slide 15: LISE++ history : DOS-version
In 1998 the MS-DOS version with 14 C++ files and less than 10 000 lines of code,
and grew on MS Windows (2016) to 615 files, about 400 000 lines,
and size of ~69 MB after Installation.
LISE REFERENCE MANUAL
Version 2.2 - June 8, 1992 ….
LISE is a DOS-based software running on any IBM compatible PC. It runs under DOS 3.1 and following versions, and only needs 640 kbytes of memory. The speed of the program depends greatly on the CPU type, speed and configuration. The use of a co-processor is greatly recommended: the program uses FFT (Fast Fourier Transform) algorithms which contain extensive floating-point operations.The last version has been developed on a 386-SX at 16 MHz with a co-processor which provides a reasonable speed (about 1 second per transmission calculation).
1986-1990
D.Bazin, GANIL
v.1.0-1.*
1990-1992
D.Bazin, MSU
O.Sorlin, Orsay
v.2.1-2.3
1994-1997
O.T., GANIL/Dubna
v.2.3 – 2.9
Named after the LISE separator @
LISE  Ligne d’Ions Super Epluches (fr) (Line of full-stripped ions)

## Slide 16: LISE++ history : MS Windows
LISE operates under MS Windows
1998
O.T., GANIL/Dubna
v.3.1
1999-2000
O.T., GANIL
v.3.2-4.9
Active development of the LISE code stimulated by M.Lewitowicz
2001
NSCL / MSU
v.4.10 –5.12
Active development of the LISE code stimulated by B.Sherrill.
Abrasion-Ablation model construction
2003
NSCL / MSU
v.6
LISE++ is the new generation of the LISE code, which allows the creation of a spectrometer through the use of different “blocks”.
RF separation system.
Abrasion – Fission.
Fusion – Fission
Monte Carlo calculation of fragment transmission
2018
NSCL / MSU
v.10.1
20...
NSCL / MSU
v.7-10
Optics calculation up to 2nd order Beam Optics Optimization (incl. 2nd order)
Wider opportunities
LISE
LISE++
Feel the
difference...
0.84”
0.93”

## Slide 17: LISE++ : Statistics, Geography

## Slide 18: Application : Energy region and Facilities
The LISE++ code may be applied at low, medium, and high-energy facilities (fragment- and recoil-separators with electrostatic and/or magnetic selections).
SECAR, MSU
DRAGON, Canada
MARS,
TAMU, USA
PRISMA, Italy
S3, France
SHELS, Russia
BigRIPS+ZeroDegree, Japan
SuperFRS_HEB, Germany

## Slide 19: Fragment Separator Construction
with different sections called "blocks" (magnetic and electric multipoles, solenoid, velocity filter, RF deflector and buncher, material in beam, drift, rotation element, and others).
a user-friendly interface that helps to seamlessly construct a fragment separator from the different blocks.
Configuration: A1900_S800BL (2nd order) 164 blocks
Magnetic dipole (to bend)
Magnetic quadrupole (to focus)
Slits (to select)
Detector

## Slide 20: LISE++ package
Besides analytical calculation of the transmission and yields of fragments

## Slide 21
Are you ready?

## Slide 22: Rare isotope beams: Basic principle of operation
1. Production
2. Separation
3. Registration, Identification

## Slide 23: 1
Production

## Slide 24: Production
Fragment of interest 58Ca
Choice of place for the experiment A1900 @ NSCL default configuration
Settings
  Reaction mechanism Projectile fragmentation > 95% experiments @ MSU
  Beam
  Target
  Charge state model no charge states assumed at these energies in this Z-region
  Energy loss model default ATIMA
  Secondary reactions in target no assumed at these energies

## Slide 25: Projectile Fragmentation
projectile
target
abrasion
ablation
projectile-like excited fragment
final fragment
58Ca
70Ge (38n+32p)
76Ge (44n+32p)
58Ca (38n+20p)
-10p
-10p
-6n
Potential beams
Beam should be a stable isotope
with more neutrons and protons
What is more probable:
To strip 10p and 6n or only 10p?
What factor?
Duke or Kansas? What score?

## Slide 26: Primary beam choice
What is more probable:
To strip 10p and 6n or only 10p?
What factor?
Conclusion: a primary beam should be more neutron-rich
http://www.nscl.msu.edu/users/beams.html
70Ge (38n+32p) → -10p → P = 2.1e-5
76Ge (44n+32p) → -10p,-6n → P = 1.3e-2
P(76Ge) / P(70Ge) = 600 !!!!
What beam from the NSCL list of available beams is more favorable to obtain a 58Ca beam?

## Slide 27: Primary beam settings
What beam from the NSCL list of available beams is more favorable to obtain a 58Ca beam?
Answer: 82Se & 76Ge are even
We observed 2 events in the NSCL experiments with a 82Se beam, and with a 76Ge beam.
82Se beam is more preferable to explore nuclei above calcium, below calcium a 76Ge beam.
But, recently the MSU & RIKEN collaboration has observed two 60Ca events even with a 70Zn beam. No 82Se and 76Ge beams available currently in RIKEN.
So, let’s select a 82Se beam
for our purpose
for all icons in the toolbar and in the production panel
there are corresponding commands in the menu

## Slide 28: Target settings
    Heavy target : larger cross sections
    Light targets have more nuclei per electron, hence larger nuclear interaction probability at fixed electronic slowing down than heavy target
    Overall case for projectile fragmentation: (s Nt ) light > (s Nt ) heavy
    Chemical and physical properties of material as melting point, thermal conductivity etc, so lifetime of Be target >> lifetime of equivalent Ta target
    Charge state distribution after target: light targets provide higher average q of ions * using strippers after heavy targets
    Dissipation process larger with heavy targets so 40Mg and 44Si been have observed in 48Ca+W
Projectile fragmentation case:
    This favors light targets (NSCL uses Be)
Ratio between target thickness and projectile range (in target)
(range = thickness required to stop a particle)
d/R ~ 0.3-0.35 for maximum fragment yield
Special utility “Optimum target”

## Slide 29: 1
Selection

## Slide 30: Yield after target
How do we select 58Ca?
Example:
82Se→ 58Ca
K500
K1200
production
target
ion sources
Coupling line
stripping
foil
82Se32+
140 MeV/u
0.4 KW
82Se13+
12.24 MeV/u
Menu “1D-plot” → “Transmission Characteristics”

## Slide 31: Fragment-separator A1900
Changing the I2 slits size,
we change the momentum acceptance
max
82Se (140 MeV/u) + Be (443mg/cm2)  **Ca
After target
Momentum slits
Settings
on 58Ca
magnetic
dipole

## Slide 32: B (magnetic rigidity) selection
Tune separator for setting fragment
After Image2 slits
It corresponds to 2 events/day, but in reality it will be less (“calcium” anomaly)
Still very high. DAQ rate should less 1000 cps

## Slide 33: “Wedge” selection (energy loss difference)
www-pdg.lbl.gov
Atomic
number of
fragment
Fragment
velocity
Then higher Z or smaller velocity, then larger dE/dx (in 10-100 MeV/u energy region)
“Wedge” = wedge-shaped degrader
+2.5%
-2.5%

## Slide 34: Wedge selection (energy loss difference)
Tune separator for setting fragment
After Focal Plain slits
Fragment production in wedge
FRIB : the second wedge separation stage to eliminate these products

## Slide 35: Selection summary
After Focal Plain slits
“Wedge” selection
After Image2 slits
B selection
After Target

## Slide 36: 1
Identification

## Slide 37: Particle IDentification
What do we want to know?
A
Z
Q
Energy (property of incoming ion in detectors)
What do we measure?
Total kinetic energy
Magnetic (electric) rigidity
Energy loss in detector
Velocity (time of flight)
In our case (low Z, E=140 MeV/u) we assume Q=Z, so we do need only 3 values to measure
Courtesy by A.Stolz
Time of flight
Magnetic rigidity
dE
TKE

## Slide 38: Correlation plots and B-selection
F
Ne
O
19F
20F
21F
22F
18O
19O
20O
21O
17N
18N
19N
100% momentum acceptance
No isotope separation
21F
22F
18O
19O
20O
21O
17N
18N
19N
21F
22F
18O
19O
20O
21O
17N
18N
19N
p/p=0.6%
Settings on 20O
Good isotope separation

## Slide 39: Obtaining A, Z, q
The atomic number is determined from the combination of energy loss (Е) and time of flights (TOF) values according to the Bethe formula:
The fragment mass can be extracted in atomic units from the relativistic formula:
where TKE is calculated as a sum of the energy loss values in each of the detectors in a multilayer telescope stopping the products. The charge state (Q) of the ion evaluated from a relation based on the TKE, velocity and magnetic rigidity values:

## Slide 40: Momentum acceptance
p/p=1%
ToF
p/p=5%
ToF
dE
dE
Z
A/q
Z and A/q resolution will be the same in spite of momentum acceptance value

## Slide 41: 76Ge(130MeV/u) + W,Be : PID, resolution
For all particles stopped in the Si-telescope in the production runs
OT et al. Phys.Rev.Lett. 102, 142501 (2009)
OT et al. Phys.Rev.C. 80, 034609 (2009)

## Slide 42: Particle identification assignments
Calibration with the primary beam (or other reference line as sources)
Unbound nuclei in the table of nuclides
Stopped fragment tagging with isomeric gamma-rays
In-flight fragment tagging with prompt gamma
X-ray from ions passing material
Laser induced fluorescence
Precise isobar selection with known masses

## Slide 43: Calibration with the primary beam
Useful then the fragment of interest is close to the projectile

## Slide 44: Unbound nuclei in the table of nuclides

## Slide 45: Stopped fragment tagging with isomeric gamma-rays

## Slide 46: Stopped fragment tagging with isomeric gamma-rays
NSCL #05120
208Pb (86 MeV/u) + Be

## Slide 47: Almost finished!
A link on this presentation can be found on the home page of the LISE++ site.
There you can also find the “First steps” manual and the detailed course of lectures
"Production of Fast Rare Ion Beams”.
Yes, we did it!

## Slide 48: Next Laboratory Wide Meeting
Questions?
Questions are always good!
62Ca at FRIB.
Where I can find a FRIB fragment separator configuration for LISE++ ??
A u planning a “Rare isotope rap” sequel?

## Slide 49: The End
“How to Make Rare Isotope Beams at Home”
Directed by Oleg Tarasov
Produced by NSCL/MSU, NSF
Story by Oleg Tarasov
Brad Sherrill
Written by Oleg Tarasov
Consulted Brad Sherrill
Alexandra Gade
Starring
Brad Sherrill Cat “Varya”
Theatrical Release poster
Production Company LISE++ pictures studio
Distributed by “FRIB/NSCL Staff Information Talk” group
Release date April 4, 2018 (United States)
Running time 30 minutes
Images from Rare Isotope Rap by “alpinekat” @ youtube https://www.youtube.com/watch?v=677ZmPEFIXE were used