## Slide 1: LISE Rate Reader + Comparison to Experiment
Kenny Haak

## Slide 2: Foreword
The goal of this code is to read results files from LISE (transmission values) and then plot them against experimentally measured rates
In order to have the LISE values and Experimental values show up on the same scale, you need to set your beam rate in the LISE file roughly equal to the total number of beam counts during that given experimental run
The end goal is a comparison plot like this
Here there is even a built-in shifting function being used to correct the underlying errors in the charge state model
To see more figures like this, reference my thesis

## Slide 3: Software Versions
Double check your versions

## Slide 4: Preparing the LISE File
Make your desired settings in the LISE file
Calculate transmission of all products
Then follow this:
This will make your LISE rate file with extension res4

## Slide 5: Preparing Experimental Yields
Count the total observed events for each identified nuclide blob
  You can use the 1D_fitter script I made if you reduced your experimental data down to 1D spectra
  Technically you could rewrite the MonteCarlo reader script I made to count 2D spectra as well, but that would require additional work
Organize it into an excel file with the following format:

## Slide 6: Initializing
Set your paths and define key variables and flags
You can see how I organized my data in the home directory
Feel free to organize and access your data however you wish
Variables & Flags:
  dset  For my data organization
  param  This allows you to compare the upper and lower bound of a given parameter adjustment such as changing target thickness
  SHIFT  Normalize the LISE data to the experimental data
  SAVE  Save the plots to a png file in your working directory

## Slide 7: Filtering and Matching Data
You can Filters to your experimental data if that is necessary
  Here we take out the primary beam and only show He-like charge state Z-q = 2
You want to compare all present experimental data to LISE
So we also look for an overlap between the two data sets and remove anything that doesn’t have a value in both experimental and LISE data
Here are the results

## Slide 8: Visualizing Parameter Variation
You can set a parameter to vary and plot the upper and lower bound of those variations
To do this you need to follow the same file structure I have in my LISE_Rates directory
Each adjusted parameter has its own directory
Within parameter directory, the naming convention goes as follows
Then simply change the param variable to the name of the directory, and voila
An alternative to this is to just run the main code with param = none and just adjust the LISE file every time. To see a result of this see Figure 3.8 of my thesis

## Slide 9: Correcting Charge State Normalizations
There were significant charge state discrepancies in the 198Pt exp at NSCL
  K. Haak et al., PRC 108 (2023) 034608
  Also see Thesis
These were corrected with Monte Carlo calculations for targets below equilibrium thickness
But the Ni target data was at equilibrium and the charge state values simply needed to be shifted
You can turn the SHIFT flag ON, and it will shift each state individually to experiment values with a log chi squared minimization
However, it is then the global normalization is uncertain, I have provided an UnNormalized version that takes the shifted values and aligns them with the most populated charge state (He-like in this case)

## Slide 10: Afterword
There is a final cell in this code that was meant to scan for parameters that should be considered in the error evaluation when estimating transmission error bars with LISE
This method works by looks for incredibly tiny transmissions and providing the point in the separator where these tiny transmissions occur
This is most likely done better with varying each and every parameter and observing the change in transmission of most products as a whole
This is really a food for though
Here this shows how small the transmissions are at the FS slits position