## Slide 1: Peak Fitter
Kenny Haak

## Slide 2: Foreword
This code fits one-dimensional histograms with a series of Gaussian functions
The value of this routine is to accurately events corresponding to a given PID (regularly drawn contours will fail to disentangle the overlapping tails of the distributions)
What makes this fitting function special is not that it has unlimited flexibility to change the parameters of each gaussian, but in fact there are restraints that correspond to real physical factors
  One fixed width – This means that there is a single width for all peaks (they all share the same underlying physical resolution)
  Integer centers – Identified peaks correspond to isotopes which have a whole integer number of protons, neutron, and electrons
  Constant (or Linear) spacing – Ideally your identified spectra should be well calibrated, but if it still needs a final shift and slope adjustment, this routine will calibrate the 1-D axis for you

## Slide 3: Initialize
Make sure you have the same versions

## Slide 4: Optimal Binning
The first actual cell allows you to play around with different bin widths
For this to be useful, your original spectra should be exported from SpecTk with the finest possible resolution
To run, simply set the file path and then change the BINS parameter
You will notice there are two plots at the bottom, this code simply shows you the default binning in which you exported from SpecTk and your new binning
There is an analytical function for optimal binning that depends on the counts and width of your peaks… Ask Isaiah

## Slide 5: Binning 2
The next cell allows you to change binning to a spa file and have it automatically resaved in xlsx format

## Slide 6: Finding Peaks
The next cell will mark every peak found in a given spectrum
First you should set the top two parameters
  BINS – You can redefine here or keep same as before
  min_gap – This is the minimum spacing in which you will allow the program to “find another peak”. I find 0.85 is reasonable but this depends on the resolution of your data
Each peak found is indicated with an orange X

## Slide 7: Fitting Peaks
The next cell is setup to plot a fitted peak figure that is acceptable for use in a publication so there is a large matplotlib settings preamble
After that you set all important parameters
  BINS and min_gap as before
  xmin / xmax – This is the range the figure will be plotted on; you need to set this manually to actually see the data
  sig – This is the initial condition for that “one fixed width” mentioned in the first slide of this document
  l / u – The lower and upper bounds for the fitting parameters
    Slope – for linearly fitting the spectra to linearly spaced integer centers
    Yint – the shifting part of the linear fit
    Sig – One Fixed Width

## Slide 8: Fitting Peaks 2
The results of the fit will be printed below along with the final figure
First you have the counts in each peak
  This is the data you came here for! Now go put that into your cross section calculation!
Next you can see how the one dimension of the spectra was linearly transformed with the slope and yint parameters
The next two lines show you the actual location of each peak and where they SHOULD be (on integer values)
  This functionality is unnecessary if you have your PID spectra properly calibrated, but we all know how picky the source code of SpecTcl can be when trying to calibrate
And finally you get the single fixed width in Sigma

## Slide 9: Binning 3
You can build on this code
One such example is writing a loop for multiple bin widths to compare a bunch of options all at once
And would you look at that, there is the analytical function for optimal bin width here
  IQR – Inter Quartile Range
  n – number of counts in a given peak
The issue with this expression is that it changes based on the number of counts in a peak
Not all peaks have consistently the same statistics
So while wider binning will look good for the low stat peaks, then the high stat peaks look funny
Therefore a range of values are tried here

## Slide 10: Appendix
The last two cells don’t have anything to do with peak fitting
But they CAN read in 2-D spectra files and plot them
In fact the final cell is the code that generated the “famous” 5 new isotopes figure for
  O.B. Tarasov et al., PRL 132 (2024) 072501
Someday it would be nice to fit 2-D plots with 2-D gaussian as opposed to 1-D plots…
It is possible, you need an AI clustering script and efficient coding of the fitting algorithm
Oleg made the BI program in LISE which does a decent job at finding and providing parameters for 2D peaks
But without being able to capture each peak, I was unable to make use of it in my analysis